## Slide 1: C-ITS
Awareness Driving

## Slide 2
Awareness Driving
Similar examples of this is “Waze” (Traffic navigation app).
Without a user, there is no notice of an accident.

## Slide 3
Awareness Driving
Take the user out of the notification process.
Ideal for scenarios like:
  Dangerous Situation Warning
  Stationary Vehicle Warning
  Pre-/Postcrash Warning

## Slide 4
HLN – SV Scenario
Hazardous Locations Notification – Stationary Vehicle: describes the use case of a broken-down car in the road.
DENM (Decentralized Environmental Notification Message): used to inform the infrastructure and alert vehicles.
Vehicle components in cooperation with a C-ITS OBU (Onboard Unit) notify nearby vehicles and RSUs (Roadside Unit) of the situation

## Slide 5: Hardware Automotive Control Units Distribution
Prev. Control Units or Modules were connected all over the vehicle. Now a more optimized architecture is being used.
Distributions can be such as:
  Rear Zone
  Front Zone
  Central Zone / Cabin Zone

## Slide 6: Hardware Car

## Slide 7: Front Zone

## Slide 8: Central Zone

## Slide 9: Rear Zone

## Slide 10: Software DTC (Diagnostic Trouble Codes)
Diagnostic Trouble Codes or OBD-II or J1939.
This codes are the way of communication of the vehicle to let the user what is happening inside. Notify you if there is a problem.
Using a telematics control unit (TCU), app or a gateway. You can access this codes to monitor the vehicle.
Fig. 8, DTC Code.

## Slide 11: DTC (Diagnostic Trouble Codes)
First Character.
  The part of the vehicle that has a fault.
Second Character
  0: Standardized code.
  1: Manufacturer-specific code.
Third Character
  The subsystem of the vehicle that has a fault.
Fourth and Fifth Character
  Exact problem that is active.
  Values from 0-99.
Fig. 9, DTC Code.

## Slide 12: Software Model
The OBU communicates with the vehicle using mainly the fault memory area, which contains the Diagnostic Trouble Codes.

## Slide 13: OBU
Onboard Unit providing C-ITS capabilities
Modeled after Commsignia’s ITS-OB4
Integrated into existing vehicle
Communicates mainly through CAN/OBD-II
Fig. 10, Commsignia OBU Ports
Fig. 9, Commsignia OBU

## Slide 14: OBU - Hardware
Fig. 11, Commsignia OBU Architecture

## Slide 15: OBU - Software
The software checks for faults and communicates with the backend
Communication is either alerting backend of own fault or receiving info about another SV

## Slide 16: RSU
Roadside Unit facilitates communication between road users and infrastructure
Modeled after Commsignia’s ITS-RS4
Architecture is very similar to Commsignia’s ITS-OB4
Fig. 12, Commsignia RSU

## Slide 17: RSU - Hardware
Fig. 13, Commsignia RSU Architecture

## Slide 18: RSU - Software
RSU mainly handles propagation of messages between environment and infrastructure in this scenario

## Slide 19: Further Work
DENM messages can also specify lane position information
This information could be used by ADAS systems and autonomous vehicles to adapt the vehicle’s driving lane.

## Slide 20: Conclusion
C-ITS improves traffic safety and takes the user out of the notification process.
The Hazardous Locations Notification – Stationary Vehicle alerts drivers of a broken-down vehicle in the road.
For the model, a vehicle with three control unit zones was considered.
OBU and RSU units were modeled after Commsignia’s products.
Integration of lane position builds towards fully autonomous vehicles.

## Slide 21: Thank You!
Questions?
Project files are also available on GitHub:
  https://github.com/LF-RoGu/Model-Base-Systems

## Slide 22
Fig. 1, https://www.car-2-car.org/fileadmin/_processed_/2/9/csm_Dangerous_Situation_Warning_010b9e61f5.jpg
Fig. 2, https://www.waze.com/website/assets/packs/media/images/og_rebrand/whatsapp-65b8f38489f59ff7ecf15b3655a320df.png
Fig. 3, https://www.researchgate.net/figure/C-ITS-System-Components_fig2_333254227
Fig. 4, https://www.smfmotor.com/wp-content/uploads/2021/03/What-to-do-in-a-car-breakdown.jpg
Fig. 5-7, https://www.bosch-mobility.com/en/solutions/control-units/zone-ecu/
Fig. 8, https://www.autopi.io/glossary/diagnostic-trouble-codes/
Fig. 9, https://www.commsignia.com/wp-content/uploads/2020/11/hardware_002_transparent.png
Fig. 10, https://www.commsignia.com/wp-content/uploads/2020/11/green_bg_obu_2021.jpg
Fig. 11, https://www.commsignia.com/wp-content/uploads/2020/11/obu_architecture_outlined.svg
Fig. 12, https://www.commsignia.com/wp-content/uploads/2020/11/green_bg_rsu.jpg
Fig. 13, https://www.commsignia.com/wp-content/uploads/2020/11/rsu_architecture_outlined.svg